## Slide 1: What is Neon? What is a SIMD Engine?

## Slide 2: Foundational study
ARM Architecture
ARM32/64
Understanding SIMD
Neon ISA
Neon Intrinsics

## Slide 3: NEON – Key Features:
Advanced SIMD architecture extension.
32 x 128bit(V0 – V31) vector registers for Aarch64.
Neon Intrinsics – C/C++ function calls replacing Neon Instructions.
2x64bit, 4x32bit, 8x16bit or 16x8bit int can be operated simultaneously.

## Slide 4: But what about SVE?
The Next Gen SIMD - Scalable Vector Extension
?

## Slide 5: Neon VS SVE
Neon
128bit vector register
Only Load/Store
Fixed vector length
SVE
128 – 2048 bit register
Provides Gather/Scatter
Vector Length Agnostic

## Slide 6: But why SVE exactly?
Aarch64
(Scalar) –
10x32 bit regs
Neon –
2x128 bit vector reg
+ 2x32 bit scalar reg
SVE/SVE2 –
3x128 bit VLA vector registers with an adjustable predicate
Computing ten chunks of 32-bit data?

## Slide 7: SVE/SVE2 Key Features:
Vector Length Agnostic.
Write once - Compile once.
Gather-load and Scatter-store.
32 x Scalable(128 - 2048) vector registers(Z0 – Z31).
Scalable predicate registers.
FFR(First Fault Register).
Predicate driven loop control and management.

## Slide 8: SVE2
Superset of Neon and SVE.
More function domains in data-level parallelism.
Includes Neon features like complex arithmetic while inheriting SVE features.
More vectorization flexibility.
More application areas.

## Slide 9: How to program and compile?
Intrinsics
#arm_sve.h
#arm_neon.h
Cross-compiler
Arm Clang
Arm GCC
Assembly Instructions?
Mov w8, 20
addvl x9, x29, #2
Str w8,[x9,24]
svld1(Pg,&a[i];
svmul_x(Pg, va,2.0);